## Slide 1: Deriving Above Ground Biomass using Modis NDVI in Google Earth Engine
Sandy 3 Allotment

## Slide 2: Goals
Develop a way to estimate above ground biomass (AGB) in Google Earth Engine using NDVI data at Sandy-3 Allotment
Develop periodic relationships between water balance variables and NDVI at Sandy-3 Allotment

## Slide 3: Data Sources
CARE HQ daily station data
MODIS Terra 16-Day
Daymet daily 1km at Sandy 3
  Used to fill blank missing data in CARE HQ daily station data
  Vp, SWE, and sRad (incorporated through 2020)

## Slide 4: Water balance/NDVI relationship analyses
Growing Season Periodic Linear Relationships
  K-fold (5) Cross Validation
  Metrics of Comparison: r2 & Root Mean Squared Error
ARIMAX (single & Multivariate)
  Train Data = 0.75, Test Data =0.25 (last 5 years)
  Examined using 0 lags
  Metrics of Comparison: Root Mean Squared Error
Earth.Google.com

## Slide 5: Overview of Sandy-3 Allotment

## Slide 6: June NDVI from 2000-2021 at Sandy 3 Allotment

## Slide 7: Nakano et. Al. established a strong linear relationship between Modis NDVI data and AGB in semi-arid grasslands of Mongolia [1].
R2 = 0.861 [1]
AGB [g/m^2] = -38.3 + (NDVI*277.9) [1]
https://www.blm.gov/programs/natural-resources/rangeland-and-grazing/rangeland-health/utah

## Slide 8: GEE Script to Extract NDVI and AGB from Sandy 3 allotment
https://code.earthengine.google.com/3df4c67181acdd06ad79279bc4f24107

## Slide 9: Extracting AGB [lb/acre] from GEE Script
Step 1: Run GEE Script
Step 2: Go to Tasks panel and select Run next to AGB timeSeries
Step 3: Select Drive and click Run on pop up. This will send the time series CSV to your Google Drive where it can then be downloaded

## Slide 10: Comparison of Modis Derived AGB and Rangeland App AGB

## Slide 11: Comparison of Modis Derived AGB and Rangeland App AGB

## Slide 12: Periodic relationships between NDVI and water balance variables during growing season
Data split into 16-day periods based on Modis imaging collection windows (23 periods altogether)
Growing season from March to October
5-fold cross validation
Average of train data r2 values after cross validation reported and used to determine best predictor during each period
Average of test data rMSE after cross validation reported

## Slide 13: Modis derived NDVI data from 2016-2021 growing seasons

## Slide 14: Modis derived NDVI with Savitsky Golay smoothing filter applied

## Slide 15: Comparison of rMSE ARIMAX models with different features
2000 – 2015 Growing Season data used to train Arimax models
2016 – 2021 data used as hold out test data in order to calculate

## Slide 16: Soil Moisture is predictor with lowest Root MSE
rMSE = 0.0136762

## Slide 17: Conclusions
Modis derived NDVI can be used to approximate above ground biomass in the Sandy-3 allotment
Strong linear relationships between periodic water balance variables and NDVI persist from late April through July.
Water balance variables can be used as a proxy for NDVI, especially during the height of the growing season (May 25 to June 25).
Single variable linear relationships showed lower root mean squared error with test data than Arimax models

## Slide 18: Future Areas of Exploration
Collect clippings from Sandy-3 allotment to validate AGB estimates, or build site specific relationship between NDVI and AGB
Developing Water balance relationships with Gridmet data to be able to forecast AGB at the Sandy-3 allotment 30 days out.

## Slide 19: References
[1] Nakano, T., Bavuudorj, B., G. Urianhai, N., Shinoda, A. (2013). Monitoring aboveground biomass in semiarid grasslands using MODIS images. Journal of Agricultural Meteorology, 69 (1), 33–39.